## Slide 1
Lessons Learned and best practices – Engineering a global dual stack and DDoS Mitigation infrastructure
Raju Raghavan . S
TATA COMMUNICATIONS
MENOG – 13
22 Sep 2013

## Slide 2: Agenda
Key Global Trends
The Context
The network journey / key learnings
Summary

## Slide 3: Tata Communications - Context
Key benefit
Over 219 PoPs in 31 countries
6th largest global IP Service Provider
13 Terabits of round the globe owned cable system.
Global IP Service Provider - 6,100G of backbone capacity
Notes: Network to deliver traffic spanning the world, nonstop.
Owner of submarine cable capacity : easy upgrade when capacity required
Major Backbone ownership :
TGN-Atlantic
TGN-Pacific
TGN-IA (intra Asia)
APCN-2 (Asia)
TIC (Singapore-India)
India NLD network
SMW4, TGN-EA, IMEWE : to Europe
WACS, Sat3, Safe, Seacom : Africa
Europe : TCL owned capacity : Marseille, Paris, Madrid, Lisbon, London, Amsterdam, Frankfurt
London-Paris-Amsterdam-Frankfurt: 12x10G ring

## Slide 4: Challenging Global Trends drive innovation in network planning
250K hits per second
Zero Tolerance
Exponential traffic growth leads to shorter planning cycles

## Slide 5: Impact of the global trends on SP infrastructure
Planning for
Traffic
Growth
Planning for
Zero
Tolerance
Capacity – 100G, 40G, 10G, 1G, STM16, STM4.,
Load Balancing – LAG, ECMP, entropy label.
Data Plane’s effect on Control plane
Control Plane’s effect on Data plane
Data Plane
Control Plane
CPU
QoS TCAM
FIB
MFIB
LFIB
Adjacency
L2FIB
Backbone / Peer / customer link Utilization
Netflow / sFlow / jFlow / IPFIX
encrypted flow, L2 PW Flow, giant flow
BFD NP Scale
Fast SPF calculations
BGP ADD Path
BFD
FRR
EOAM
G.8032
xSTP
LFA
BGP Best External
Vicious
Cycle

## Slide 6: Network Analytics and focused instrumentation unravel interesting perspectives
Chart: 
| FIB | QoS | Routing Context | Access | BFD | lambdas | 40G / 100G | Switching Capacity
Public Cloud / Domain | 300 | 8 | 100 | 100 | 100 | 1000 | 1000 | 1000
Private Cloud / Domain | 1000 | 2000 | 1500 | 1000 | 1500 | 10 | 10 | 10
Control Plane
Data Plane
100G / 40G / LAGs
Hot potato Routing, Peering management,
Multi Gigabit DDoS Attacks, IPv6
Public Cloud / Domain
Private Cloud / Domain
VPNs, Fast Convergence, BFD/LFA
Multiple QoS requirements
Application Optimization and SLAs, zero tolerance

## Slide 7: Food for thought
Tata Communications deploys both converged and de-converged architecture in different parts of the network
High Traffic vs. high Control plane intensive geographies
Does economics play a role?
How does it affect planning cycles?
Converged Network Model
De-Converged Network Model

## Slide 8: Globally ~2500 large DDoS attacks happen every day (about 2.5 Mn attacks every year)
BOSS
BOT Chief
Infected Computer

## Slide 9: DDoS attacks can be mitigated using behavioral analysis, black list filtering ,protocol validation techniques etc., in a DDoS Scrubbing Farm
Zombies
Zombies
Zombies
Zombies
Zombies
Target / Victim
Zombies
Clean Traffic
DDOS Scrubbing farm
How can we defend DDoS attacks?

## Slide 10: + In premise DDoS mitigation infrastructure are not an alternative for obvious reasons . + Firewall, IDS, IPS , Antivirus are a different ballgame
Zombies
Zombies
Zombies
Zombies
Target
Zombies
Clean Traffic
Zombies
Regional Scrubbing Farm
Cloud based distributed mitigation vs. in premise mitigation
So Tata Communications has deployed a global distributed scrubbing farm that scrubs attack traffic regionally

## Slide 11: Anycast on-ramping
Target
Zombies
Advertise /32 of the target
GRE Tunnel
GRE Tunnel
Anycast GRE
How can you seamlessly add / remove scrubbing farms as the attack evolves quickly?

## Slide 12: Case Study | Large Service provider
Large Service Provider in Asia .
Typical traffic towards one particular destination – 35- 40 Mbps
20Gbps Attack from Europe and American zombies

## Slide 13: Case Study | Large Service provider
Bandwidth Attack – Avg Packet size = 1KB

## Slide 14
14
Tata Communications IPv6 Context

## Slide 15: Learnings from the IPv6 deployment journey
Global backbone
Have you tried deploying 6 PE with a hierarchical design?
  Swapping 6PE service labels have no standard mechanisms across leading vendors .
  Every vendor has a different way of generating the 6PE service labels
Tata Communications deploys a global native dual stack backbone with native IPv6 IGP and BGP

## Slide 16: Global Dual Stack IGP deployment
V4 and v6 Topology
V4 Topology
V6 Topology
Tata Communication's deploys Multi-topology ISIS
This gives us the flexibility of steering IPv6 and IPv4 traffic on different topologies as vendors evolved their IPv6 support / maturity
Integrated Topology view
Multi Topology view

## Slide 17: Summary
Innovation in network engineering is being driven by challenging global network trends of exponential traffic growth vis a vis zero tolerance expectations
Network analytics of control and data plane uncovers interesting perspectives related to technical behavior of various market segments . These insights can be innovatively applied in network engineering/design.
Tackling todays multi gigabit DDoS attacks is best done using a global distributed / intelligent DDoS scrubbing infrastructure. In premise DDoS mitigation infrastructure are not an alternative.

## Slide 18: Summary
Since we started our IPv6 Network journey 10 years back , we had several learnings that prompted us to deploy a unique global dual stack and multi-topology infrastructure
Build your network infrastructure not based on “generic best practices” but based on in-depth contextual analytics / focused instrumentation and technical / business merit !

## Slide 19
Thank you and Happy Innovating for your network!