## Slide 1: IPv6 Deployment Case of Sudan/SudREN
شبكة البحث العلمي والتعليم السودانية
Sudanese Research and Education Network
Middle East Network Operators Group (MENOG 15)
1-2 April 2015, Dubai, UAE

## Slide 2: Sudanese Experience Toward IPv6

## Slide 3: Activities
    1st IPv6 Workshop; 24June, 2010
    As a side event of AREGNET Meeting.
    2nd IPv6 Workshop; 1 August, 2010
    Publish the Sudanese IPv6 Migration Plan (2011-2015).
    Formation of the SDv6TF.
    3rd IPv6 Workshop; 1-4 November, 2010
    2nd IPv6 Training.
    Internet Governances day.
    4th IPv6 Workshop; 27 October, 2011
    Evaluation of the IPv6 Deployment in Sudan on 10 Major Information Network Operator

## Slide 4: National IPv6 Training Center

## Slide 5: Achievements
Number of Session Organized | 17
Total Number of Attends | +400
Exam Taken | 218
CNE6 Level-1 Certified | 182

## Slide 6: Activities
    5th IPv6 Workshop; 26-30 October, 2013
    IPv6 Workshop for Yemeni Delegations

## Slide 7: IPv6 Deployment
    Development of the National IPv6 Migration Plan (2011-2015)
    Participate on IPv6 Events (ITU, ICANN, AfriNIC, NAV6)
    Formation of the SDv6TF
    Five workshops are organized
    Collaborate with NAv6 in continuous training program
    Operators are IPv6 Enable/Ready.
    Host AfriNIC-17

## Slide 8: Development in IPv6 Assignment

## Slide 9: IPv6 Traffic

## Slide 10: Join the SDv6TF @facebook.com

## Slide 11: SudREN at a Glance
SudREN is licensed ISP dedicated to the Sudanese research and educational intuitions.
    3 STM-1 (450 Mb) Total Bandwidth to the upstream providers,
    63+ Member Institution are connected via Layer-3 MPLS VPN on Local carries providers (Sudatel, Canar),
SudREN has its own Numbering resources from
41.67.0.0/18
197.251.0.0/17
2c0f:fec8::/32

## Slide 12
SudREN Network
Member 1
Member 2
Member 4
Member 3
Member 63
Internet-Sudatel
200 Mbps
150Mbps
SIXP
4 Mbps
PoP1
PoP2
100 Mbps
BGP
OSPF
BGP
BGP
OSPF
OSPF
OSPF
OSPF
Fiber
Internet-Canar
BGP
BGP
BGP

## Slide 13: Resource Utilization
SudREN has a utilized of about 90% of the the 1st block and about70% of the 2nd one.
SudREN started to put a strategic plan in accordance with the National Migration Plan toward IPv6.

## Slide 14: Migration Plan
Network Analysis:
  Gather information on network infrastructure, key network equipment, servers, appliances and computers.
Define roadblocks:
  Identify the main challenges and key issues that hinder deploying IPv6.
Workarounds:
  Develop a plan to migrate to IPv6 with minimum impact on existing critical applications.
Final Plan:
  Prepare a set of strategies covering IT equipment acquisition, new critical applications, manpower resource planning and network policies to prepare for fully enabled IPv6 Network

## Slide 15
Chart: SudREN Network Analysis
| POPs | Members | Servers | Applications
% Supported | 0.5 | 0.095 | 1 | 0.8

## Slide 16: Deploying IPv6
Steps to deploy IPv6
Gateway
Internal Network (DMZ)
Enable IPv6 on SudREN internal Network
Members’ VPN
Enable IPv6 for SudREN members
Enable IPv6 on the Gateways

## Slide 17: IPv6 in the Gateways
SudREN has a native IPv6 link to the internet via (Sudatel)
Redundancy Tunnel is also available through
BGP
Internet-Sudatel
PoP1
BGP
IPv6-Link
DMZ
IPv6-Link

## Slide 18: IPv6 Addressing
Each members currently is assigned /48 IPv6 Address block, and reserved /40 for future demand.
SudREN started putting a strategy to extend its IPv6 block.
New IPv6 Addressing plan goals
  Improving routing aggregation.
  Minding future growth with contiguous address space.
  Hierarchical allocation “universities & campuses”
  Recognizing directly from the IPv6 Address what location/environment a networks belongs to.
  Reflect the organization infrastructure..

## Slide 19: IPv6 Addressing (Cont.)
New IPv6 Addressing factors and criteria
The classification of members’ institutions.
    SudREN Infrastructure (i.e. PTP, DMZ, Loopbacks …etc.)
    Universities & Colleges
    Research Institutions
    Schools (expected)
    Educational Hospitals (expected in the future)
The geographical areas in which the member are based.
    Central Area (Khartoum), Northern, Western, Southern, & Eastern
Members’ campuses listing.
    Number of campuses for each member

## Slide 20: IPv6 Addressing example
2C0F:FE | Geographical Area | Member Type | Member Name | Campuses | IP Address /48 | Meaning
2C0F:FE | 0 | 0 | 00 | 00 | 2C0F:FE00:: | University X Campus 1 in Khartoum
2C0F:FE | 0 | 0 | 00 | 01 | 2C0F:FE00:1:: | University X Campus 2 in Khartoum
……………… |  |  |  |  |  | 
2C0F:FE | 3 | 4 | 22 | 01 | 2C0F:FE34:2201:: | College X Campus 1 in North of Sudan
……………… |  |  |  |  |  | 
2C0F:FE | 6 | 0 | 00 | 03 | 2C0F:FE60:0003:: | University X Campus 3 in West of Sudan

## Slide 21: Achievements
http://sudren.edu.sd/

## Slide 22: Achievements

## Slide 23: Challenges
Coordination with upstream providers.
IPv6 is not supported in most members’ routers.
  Use of tunnels.
No Redundancy for IPv6 Connectivity in Our POPs.
IPv6 is not fully supported in both POPs Firewalls.
Temporary IPv6 vs. DHCP.

## Slide 24
شبكة البحث العلمي والتعليم السودانية
Sudanese Research and Education Network
Sami Salih
SudREN, CEO
Sami.salih@sudren.edu.sd