## Slide 1
Modern network servers
Notes: .

## Slide 2: Example network service: dk-hostmaster.dk
Small country. Small amount of traffic.
representative ccTLD deployment.

## Slide 3: Traffic as of December 2016
Per unicast server: 1,000 qps
1.3M domain names
11,000 DNSSEC signed domains (zone size!)
Total zone file size: ~190MByte raw text
Depending on the nameserver: 800-1000Mbyte in RAM
CPU load approximately 0 (except when loading a new zone)
>10Mbps continuous traffic
Data provided by dk-hostmaster.dk

## Slide 4: Operational structure
Unicast servers
a.nik.dk
b.nik.dk
c.nik.dk
l.nik.dk
Anycast clouds
7 clouds
>120 nodes
Implementation
Off the shelf Intel servers
Running FreeBSD
Resource utilisation: 2–5%

## Slide 5: Network servers
hardware considerations for network servers vs. generic-purpose servers

## Slide 6: Resources network servers care about
CPU: lots of trivial operations running in parallel
Memory and bus bandwidth
Network
Disk I/O

## Slide 7: Previous attempts at low-power, high-bandwidth CPUs
Sun T1/… (SPARCv9)
Cavium Octeon (MIPS)
Tilera, Quanta Computer, → EZChip → Mellanox
Intel Atom (x86)
32-bit ARM (ARMv7)

## Slide 8: ARM64
A new attempt at a server-grade architecture

## Slide 9: ARM64: a new attempt at server-grade CPUs
Main architecture highlights
ARMv8 – a 64-bit Instruction Set Architecture
AES instructions similar to Intel AES-NI (2GB/s AES in block mode on FreeBSD)
Standardised on-core peripherals: GIC, MSI(-X) interrupts, timer, IOMMU
Platform approach – attempt at creating unified configuration mechanisms: ACPI, UEFI
Standard server peripherals: AHCI for SATA, NVMe, Intel/Chelsio Ethernet …

## Slide 10: Commercial off-the-shelf hardware: Cavium
Cavium ThunderX CPU
48 cores (scales to 96)
16x PCIe 3 lanes
3x 40GbE or 12x 10GbE (vnic(4)) with programmable queue processing
Gigabyte server board (~$3000 USD)
1x Cavium ThunderX ARM processor
8x DDR4 DIMM slots
1x 40GbE QSFP+ LAN port and 4x 10GbE SFP+ LAN ports
4x 3.5. hot-swappable HDD/SSD bays

## Slide 11: Commercial off-the-shelf hardware: AMD
AMD A1100 CPU
AMD update to the ARM Cortex A57
SoftIron (~$600 USD)
AMD Opteron A1100 series processor (4 cores)
2x RDIMM with 8GB DDR4 DRAM
1x 1Gbit Ethernet
2x USB 3.0 ports
2x SATA 3.0 ports
1x 1TByte HDD

## Slide 12: Operating system support
ARM64 is a Tier-1 supported platform on FreeBSD
Fully supported by binary updates (freebsd-update and pkg)
Supported by security-officer and release engineering
>20,000 third-party binary software packages work out of the box
DNS on FreeBSD on ARM64
Full support by all common authoritative and recursive DNS implementations
Binary packages available for BIND9, NSD, Knot, PowerDNS and Unbound
Direct vendor support (NLNetLabs, ISC) or maintainer working closely with vendor

## Slide 13: Performance comparison
Intel Xeon
E5-2630 v4 (10 cores + HT), 128GByte RAM, 2x240GByte SSD, 2x1TByte HDD
Cost: ~$3,100 USD
Cavium ThunderX
ThunderX, 1 socket, 128GByte RAM, 4x2TByte HDD
Cost: ~$3,000 USD
LLVM clang build on FreeBSD-HEAD (pessimal workload)
ThunderX: 32 minutes total, 74,000 minutes CPU time (20h)
Xeon: 10 minutes total, 1h CPU time

## Slide 14: DNS servers spend very little timing compiling
LLVM build workload
Lots of continuous disk I/O
Gigantic memory footprint and churn
CPU load can only be parallelised to a limited extent
Authoritative DNS workload
Modest amount of disk I/O when loading zone files
Entire working data set fits in memory (true for most ccTLDs and nTLDs)
Easy to parallelise CPU load

## Slide 15: Power consumption and cooling
Traditional x86 servers
Very warm CPUs – Haswell: 135W TDP (specification), ~250W under load
Need lots of active cooling – consumes even more power
ARM64 servers
Much cooler CPUs – ThunderX: 120W TDP (specification), ~200W under load
Several vendors sell much lower power CPUs
Still need cooling – but a lot less of it!

## Slide 16: A slight digression on security
Speculative execution vulnerabilities (Meltdown / Spectre)
ARM64 is vulnerable to many of the same vulnerabilities as x86-64
On FreeBSD, both vulnerabilities have been mitigated in supported releases
Probably not a huge concern on DNS servers

## Slide 17: Conclusions
ARM64 is a viable platform for network workloads
Comparatively cheap hardware
Great for parallel network-bound workloads
Well-supported by FreeBSD and popular DNS software