## Slide 1
Impact of Carrier-Grade NAT on Web Browsing
Ali Safari Khatouni
Enrico Bocchi
Stefano Traverso
Alessandro Finamore
Valeria Di Gennaro
Marco Mellia
Maurizio Munafò
Dario Rossi
Notes: Do we need the pictures?

## Slide 2: NAT at a glance - Traditional NAT44
Internet
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.*
128.130.90.61
Public IP address
worldwide unique registered addresses
Private IP addresses
unregistered addresses
Home NAT

## Slide 3: NAT at a glance - Traditional NAT44
Internet
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.*
128.130.90.61
Public IP address
worldwide unique registered addresses
Private IP addresses
unregistered addresses
Home NAT

## Slide 4: …and Carrier Grade NAT – NAT444
ISP Subnet
Internet
Home NAT
Carrier Grade NAT
ISP subnet becomes a large private network
Home routers are assigned private IPs
The amount of required public addresses is reduced as well as cost

## Slide 5: Carrier Grade NAT (CGN)
The deployment of CGN has some implications:
Breaks the end-to-end IP connectivity
Introduces reachability problems for NAT-ted devices
  Need of successful NAT traversal techniques
  Updates of non-NAT friendly applications
Mandates the network keeps the state of the connections
Impacts negatively lawful intercept
May have performance implications
Our investigation goals
  Does CGN impact users’ browsing experience?
  Are there any benefits in not having a public IP?
  Answer with measurements

## Slide 6
Methodology
Notes: Do we need the pictures?

## Slide 7: Methodology roadmap
Large scale passive measurement
  A real ISP deployment
  Customers are offered public or private address
  Traffic monitored to extract performance metrics
Leverage statistical tools
  Collect and compare empirical probability distributions
  Check and assess eventual differences
Focus on
  Web traffic and performance

## Slide 8: Monitoring Scenario
ISP Point of Presence
Carrier-Grade
NAT
Public Addresses
Private Addresses
Internet
Passive Probe
Dataset
  1 month of real traffic recorded, October 2014
  17,000 household monitored, 40% with public IP address
  1.7Billion TCP flows, 0.7Billion HTTP requests
http://tstat.polito.it

## Slide 9: Measurements
Household
Passive Probe
TSYN
TEstablish
Time
SYN
SYN-ACK
ACK
HTTP GET
HTTP RESPONSE
ACK
TRequest
Server
TLast
TResponse
TTFB
RTT
TWHT
THROUGHPUT

## Slide 10: Assessing the Impact of CGN
Consider 9 performance metrics
Measure distinct probability distributions for each metric
  Tied to private and public households
Jensen-Shannon Divergence
Quantify the difference between a pair of probability distributions
Based on the Kullback-Leibler divergence
  Symmetric
  Bounded to finite value

## Slide 11: Jensen-Shannon Calibration
Need of a threshold to discriminate between significant and negligible differences
Calibration with:
Negexp CDF
λ0 = 1, fixed
λ1 varies [1 ÷ 8]

## Slide 12: Jensen-Shannon Calibration
Recommendations to avoid bias:
Tool calibration to avoid measurement artifacts
Adequate binning strategy
Relevant population size
Distribution samples are TCP flows
Dataset
  1.7B TCP flows
  0.7B HTTP requests

## Slide 13
Performance Metrics Analysis
Notes: Do we need the pictures?

## Slide 14: Performance Metrics – TWHT
Three Way Handshake Time (TWHT)
  Any remote server (all)
  iTunes contents (phobos.apple.com - Akamai)
  Google Search (Google.com)
Service | JS Div
All | 0.002
Phobos | 0.016
Google.com | 0.010

## Slide 15: Performance Metrics – Throughput
Service | JS Div
All | 0.001
Phobos | 0.022
Tumblr | 0.021
Three Way Handshake Time (TWHT)
Download Throughput
  Any remote server (all)
  iTunes contents (phobos.apple.com - Akamai)
  Tumblr Blogging Platform (Tumblr.com)

## Slide 16: Performance Metrics – Number of Hops
Service | JS Div
All | 0.223
Phobos | 0.689
Google.com | 0.666
Three Way Handshake Time (TWHT)
Download Throughput
Number of Hops
  Any remote server (all)
  iTunes contents (phobos.apple.com - Akamai)
  Google Search (Google.com)
Only metric showing noteworthy differences
4 hops more for private customers
Affecting any service being contacted

## Slide 17: Jensen-Shannon Results
Three intervals identified
  Significant differences JSdiv ≥ 0.1
  Noticeable differences 0.02 ≤ JSdiv < 0.1
  Negligible differences JSdiv < 0.02
Metric | Any Server | Google.com | Phobos.com
Number of Hops | 0.223 | 0.666 | 0.689
Latency (RTT) | 0.001 | 0.006 | 0.007
Establish (TWHT) | 0.002 | 0.010 | 0.016
HTTP 1st (TTFB) | 0.002 | 0.006 | 0.006
Throughput | 0.001 | - | 0.022
Number of SYN | <0.001 | <0.001 | <0.001
Out of Sequence | <0.001 | - | -
Duplicates | 0.001 | 0.001 | <0.001
Our investigation goals
  Does CGN impact users’ browsing experience?
We observe no significant impact
  Are there any benefits in not having a public IP?

## Slide 18
Benefits of having a Public / Private IP address
Notes: Do we need the pictures?

## Slide 19: Active Servers
Does the customer need IPv4 reachability?
  Is there any ISP customer running a server at home?
Detection technique
Look for customers answering at least one incoming connection
  Protocols: HTTP(S), IMAP(S), POP(S), SMTP(S)
  No P2P
Only 0.6% of customers runs servers at home

## Slide 20: Saving in IP addresses using NAT
How many active IP are present?
  Assume an idle timer of 5min at the CGN
  Active: generated one connection in the last 5min
Customer base: ~17000
Max concurrently active: ~7000
Saving due to CGN: ~60%

## Slide 21: What about PAT?
How many concurrent connection?
  Concurrent: active in the past 5 min
95% have less than 600
99% have less than 2400
Worst case have more than 20000
Possible saving (with 65k ports)
95% ok => 100x
99% ok => 27x
Worst case => 1x

## Slide 22: Conclusions
Goal: assess the impact of CGN on users’ web browsing
  Large scale passive measurements
  Multiple performance metrics considered
  Jensen Shannon to pinpoint relevant statistical differences
CGN does not harm users’ web browsing
Current investigations
  How to correctly dimension CGN and what is the saving in IPv4 address?
  Is there any implications on P2P traffic?

## Slide 23
Questions?
ali.safari@polito.it
http://www.ict-mplane.eu
Notes: Do we need the pictures?

## Slide 24: Unsolicited Traffic
What about unsolicited traffic?
How many home routers are victims of port-/net- scans?
Carrier-Grade
NAT
Public Addresses
Private Addresses
?
Compile a list of potential attackers
  Remote hosts sending TCP-SYN messages to more than 50 IPs in the PoP
Focus on destination ports with well-known services or vulnerabilities

## Slide 25: Unsolicited Traffic
Destination Port | Description | Percentage of victims in PoP | 
 |  | PRI | PUB
80 | HTTP | 1.8 | 78.5
443 | HTTP Secure (HTTPS) | 0.1 | 78.9
143 | Internet Message Access Protocol (IMAP) | <0.1 | 79.3
995 | Post Office Protocol (POP3 over SSL) | <0.1 | 79.2
25 | Simple Mail Transfer Protocol (SMTP) | 0.1 | 79.0
22 | Secure Shell (SSH) | <0.1 | 79.2
135 | MS Remote Procedure Call | <0.1 | 79.3
3389 | MS Windows Remote Desktop | 0.1 | 79.3
1433 | MS SQL Server | 0.1 | 79.3
3306 | MySQL Server | 0.1 | 79.3
445 | MS Active Directory | <0.1 | 79.2
Our investigation goals
  Does CGN impact users’ browsing experience?
  Are there any benefits in not having a public IP?
0.6% of customers needs IPv4 reachability
Public IPs are 80x more likely to be victim of attacks