## Slide 1
Segment Routing
Rasoul Mesghali CCIE#34938
Vahid Tavajjohi
MENOG 18
From HAMIM Corporation

## Slide 2: Agenda
Introduction
Technology Overview
Use Cases
Closer look at the Control and Data Plane
Traffic Protection
Traffic engineering
SRv6

## Slide 3: Introduction
MENOG 18

## Slide 4
MPLS “classic” (LDP and RSVP-TE) control-plane was too complex and lacked scalability.
LDP is redundant to the IGP and that it is better to distribute labels bound to IGP signaled prefixes in the IGP itself rather than using an independent protocol (LDP) to do it.
LDP-IGP synchronization issue, RFC 5443, RFC 6138
Overall, we would estimate that 10% of the SP market and likely 0% of the Enterprise market have used RSVP-TE and that among these deployments, the vast majority did it for FRR reasons.
The point is to look at traditional technology (LDP/RSVP_TE) applicability in IP networks in 2018. Does it fit the needs of modern IP networks?
MPLS Historical Perspective

## Slide 5
In RSVP-TE and the classic MPLS TE The objective was to create circuits whose state would be signaled hop-by-hop along the circuit path. Bandwidth would be booked hop-by-hop. Each hop’s state would be updated. The available bandwidth of each link would be flooded throughout the domain using IGP to enable distributed TE computation.
First, RSVP-TE is not ECMP-friendly.
Second, to accurately book the used bandwidth, RSVP-TE requires all the IP traffic to run within so-called “RSVP-TE tunnels”. This leads to much complexity and lack of scale in practice.
MPLS Historical Perspective

## Slide 6
1.network has enough capacity to accommodate without congestion
traffic engineering to avoid congestion is not needed. It seems obvious to write it but as we will see further, this is not the case for an RSVP-TE network.
2.In the rare cases where the traffic is larger than expected or a non-expected failure occurs, congestion occurs and a traffic engineering solution may be needed. We write “may” because it depends on the capacity planning process.
3.Some other operators may not tolerate even these rare congestions and then require a tactical traffic-engineering process.
A tactical traffic-engineering solution is a solution that is used only when needed.

## Slide 7
the classic RSVP TE solution is an “always-on” solution
This is the reason for the infamous full-mesh of RSVP-TE tunnels.
N2*K tunnels While no traffic engineering is required in the most likely situation of an IP network, the classical MPLS TE solution always requires all the IP traffic to not be switched as IP, but as MPLS TE circuits.
complexity and limited scale,
most of the time, without any gain
An analogy would be that one needs to wear his raincoat and boots every day while it rains only a few days a year.

## Slide 8: Goals and Requirements
Make things easier for operators
  Improve scale, simplify operations
  Minimize introduction complexity/disruption
Enhance service offering potential through programmability
Leverage the efficient MPLS dataplane that we have today
  Push, swap, pop
  Maintain existing label structure
Leverage all the services supported over MPLS
  Explicit routing, FRR, VPNv4/6, VPLS, L2VPN, etc
IPv6 dataplane a must, and should share parity with MPLS

## Slide 9: Operators Ask For Drastic LDP/RSVP Improvement
Simplicity
  less protocols to operate
  less protocol interactions to troubleshoot
  avoid directed LDP sessions between core routers
  deliver automated FRR for any topology
Scale
  avoid millions of labels in LDP database
  avoid millions of TE LSP’s in the network
  avoid millions of tunnels to configure

## Slide 10: Operators Ask For A Network Model Optimized For Application Interaction
Applications must be able to interact with the network
  cloud based delivery
  internet of everything
Programmatic interfaces and Orchestration
  Necessary but not sufficient
The network must respond to application interaction
  Rapidly-changing application requirements
  Virtualization
  Guaranteed SLA and Network Efficiency

## Slide 11: Segment Routing
Simple to deploy and operate
  Leverage MPLS services & hardware
  straightforward ISIS/OSPF extension to distribute labels
  LDP/RSVP not required
Provide for optimum scalability, resiliency and virtualization
SDN enabled
  simple network, highly programmable
  highly responsive

## Slide 12: Technology Overview
MENOG 18

## Slide 13
CE1
PE1
P2
P3
P4
P5
P6
P7
CE2
Segment 1
Segment
2
Segment 3
What is the meaning of Segment Routing?
PE2
10
10
20
10
Default Cost is 100

## Slide 14
CE1
PE1
P1
P2
P3
P4
P5
P6
P7
CE2
PE2
16099
24001
16007
16007
24001
16007
Segment 1
Segment
2
Segment 3
16007
24001
16007
Adj-SID Label
Prefix-SID Label
Service: L3VPN,L2VPN,6PE,6 VPE
Prefix-SID
Loopback0
Label 16099
Prefix-SID
Loopback0
Label 16007
Adj Label 24001
Default: PHP at each segment
Prefix-SIDs are global Labels
Adj-SIDs are local labels
Deviate from shortest path-Source Routing:
Traffic Engineering based on SR
SR in one Slide
PE2

## Slide 15
Let’s take a closer look

## Slide 16
Source Routing
  the source chooses a path and encodes it in the packet header as an ordered list of segments
  • the rest of the network executes the encoded instructions (In Stack of labels/IPv6 EH)
Segment: an identifier for any type of instruction
• forwarding or service
Forwarding state (segment) is established by IGP
  LDP and RSVP-TE are not required
  Agnostic to forwarding data plane: IPv6 or MPLS
MPLS Data plane is leveraged without any modification
  push, swap and pop: all that we need
  segment = label

## Slide 17
Segment Routing – Overview
• MPLS: an ordered list of segments
is represented as a stack of labels
• IPv6: an ordered list of segments is
encoded in a routing extension header
• This presentation: MPLS data plane
Segment → Label
Basic building blocks distributed
by the IGP or BGP
Paths options
Dynamic
(SPT computation)
Explicit
(expressed in the packet)
Control Plane
Routing protocols with extensions
(IS-IS,OSPF, BGP)
SDN controller
Data Plane
MPLS
(segment ID = label)
IPv6
(segment ID = V6 address)
Strict or loose path

## Slide 18
Global Segment
Any node in SR domain understands associated instruction
Each node in SR domain installs the associated instruction in its
forwarding table
MPLS: global label value in Segment Routing Global Block
(SRGB)
Local Segment
Only originating node understands associated instruction
MPLS: locally allocated label
Global and Local Segments

## Slide 19
Global Segments always distributed as a label range
(SRGB) + Index
Index must be unique in Segment Routing Domain
Best practice: same SRGB on all nodes
  “Global model”, requested by all operators
  Global Segments are global label values, simplifying network
  operations
  Default SRGB: 16,000 – 23,999
  Other vendors also use this label range
Global Segments – Global Label Indexes

## Slide 20
Types of Segment

## Slide 21
Segment
Segment
Segment
Segment
Segment
Segment
Segment
Segment
Segment
Segment
Segment
IGP Segment
Two Basic building blocks distributed by IGP:
-Prefix Segment
-Adjacency Segment
Prefix-SID (Node-SID)
Adjacency-SID
4
3
2
1
1
1
Segment

## Slide 22
6
5
2
1
7
16006
1.1.1.6/32
16006
16006
16006
16006
6
5
2
1
7
16005
16005
16005
16005
16005
1.1.1.5/32
IGP Prefix Segment
Node-SID
Shortest-path to the IGP prefix
  Equal Cost Multipath (ECMP)-
  aware
Global Segment
Label = 16000 + Index
Advertised as index
Distributed by ISIS/OSPF
Default SRGB 16000-23,999

## Slide 23: Node Segment
E advertises its node segment
  Simple ISIS/OSPF sub-TLV extension
All remote nodes install the node segment to E in the MPLS Data Plane
16065
FEC Z push 16065
swap 16065 to 16065
swap 16065 to 16065
pop 16065
A packet injected anywhere with top label 16065 will reach E via shortest-path
A
B
C
D
E

## Slide 24: Node Segment
E advertises its node segment
  simple ISIS sub-TLV extension and OSPF
All remote nodes install the node segment to E in the MPLS dataplane
16065
FEC Z push 16065
swap 16065 to 16065
swap 16065 to 16065
pop 16065
A packet injected anywhere with top label 16065 will reach E via shortest-path
Packet to E
Packet to E
16065
Packet to E
16065
Packet to E
16065
Packet to E
A
B
C
D
E

## Slide 25: Adjacency Segment
C allocates a local label and forward on the IGP adjacency
C advertises the adjacency label
Distributed by OSPF/ISIS
simple sub-TLV extension
  (https://datatracker.ietf.org/doc/draft-ietf-isis-segment-routing-extensions/)
  https://www.iana.org/assignments/isis-tlv-codepoints/isis-tlv-codepoints.xhtml
C is the only node to install the adjacency segment in MPLS dataplane
A packet injected at node 5 with label 24056 is forced through datalink 5-6
6
5
2
1
7
24057
Adj to 7
Adj to 6
24056

## Slide 26: Datalink and Bundle
Adjacency segment represents a specific datalink to an adjacent node
Adjacency segment represents a set of datalinks to the adjacent node
Pop 9003
9001 switches on blue member
9002 switches on green member
9003 load-balances on any member of the adj
Pop 9001
Pop 9002
Pop 9003
B
A

## Slide 27: A path with Adjacency Segments
Source routing along any explicit path
  stack of adjacency labels
SR provides for entire path control
9101
9105
9107
9103
9105
9101
9105
9107
9103
9105
9105
9107
9103
9105
9107
9103
9105
9103
9105
9105
7
6
5
4
3
2
1
7
7

## Slide 28: Combining Segments
24078
Packet to Z
16011
24078
Packet to Z
16011
Packet to Z
Packet to Z
16011
Packet to Z
16011
24078
16007
Packet to Z
16011
24078
16007
16007
16007
16011
16011
Adj-SID
Prefix-SID
1
5
9
3
6
8
7
11
Steer traffic on any path
through the network
Path is specified by list of
segments in packet header, a
stack of labels
No path is signaled
No per-flow state is created
For IGP – single protocol, for
BGP – AF LS
10

## Slide 29
P1
P2
P3
P4
10.20.34.0/24
GE 0/0/0/0
Prefix attached to P4 | Outgoing label in CEF? Entry in LFIB?
Prefix-SID P4 (10.100.1.4/32) | Y
Prefix-SID P4 without Node flag (10.100.3.4/32) | Y
loopback prefix without prefix-sid (10.100.4.4/32) | N
link prefix connected to P4 (10.1.45.0/24) | N
Labeling Which prefixes?
• So, this is the equivalent of LDP label prefix filtering: only
assigning/advertising labels to /32 prefixes (loopback prefixes, used by
service, (e.g. L3VPN), so BGP next hop IP addresses)
• Traffic to link prefixes is not labeled!

## Slide 30
Data
7
Dynamic path
Explicit path
High cost
Low latency
Adj SID: 46
R1
SID: 1
R2
SID: 2
SID: Segment ID
R4
SID: 4
R6
SID: 6
R7
SID: 7
R3
SID: 3
R5
SID: 5
Data
7
46
4
Explicit loose path for low latency app
No LDP, no RSVP-TE

## Slide 31
10
20
30
40
50
60
70
80
90
Anycast SID: 200
70
200
Packet
70
200
Packet
70
200
Packet
70
Packet
Packet
A group of Nodes share the same SID
Work as a “Single” router, single Label
Same Prefix advertised by multiple nodes
traffic forwarded to one of Anycast-Prefix-SID based on best IGP Path
if primary node fails,traffic is auto re-routed to other node
• Application
– ABR Protection
– Seamless MPLS
– ASBR inter-AS protection
Any-Cast SID for Node Redundancy

## Slide 32
1
2
3
4
5
6
7
8
9
10
Node 10
30410
16004
16003
Node 10
30410
16004
Node 10
30410
Node 10
30710
16007
16006
Node 10
30710
16007
Node 10
30710
Node 10
16010
16009
Node 10
16010
Node 10
14
410
BSID:
30410
SID:
30710
Binding-SIDs can be used in the following cases:
Multi-Domain (inter-domain, inter-autonomous system)
Large-Scale within a single domain
Label stack compression
BGP SR-TE Dynamic
Stitching SR-TE Polices Using Binding SID
Binding-SID
All Nodes SRGB [16000-23999]
Prefix-SID NodeX: 1600X
Binding-SID X->Y: 300XY

## Slide 33
12
11
Node SID: 16001
10
1
13
14
3
BGP Prefix Segment
BGP-Connections
Shortest-Path to the BGP Prefix
Global
16000 + Index
Signaled by BGP

## Slide 34
12
11
7
AS1
AS2
Node SID: 16001
BGP-Peering-SID
SID: 30012
5.5.5.5/32
10
1
13
14
5
2
3
Packet
18005
30012
16001
Packet
18005
30012
Packet
18005
Packet
Node SID:
18005
BGP Peering Segment
Egress Peering Engineering
Pop and Forward to the BGP Peer
Local
Signaled by BGP-LS (Topology Information) to the controller
Local Segment- Like an adjacency SID external to the IGP
Dynamically allocated but persistent
BGP-Peering-SID

## Slide 35
12
11
7
IGP-1
IGP-2
BGP-LS
5.5.5.5/32
10
1
13
14
5
2
3
Node SID:
18005
WAN Controller
SR
PCE
BGP-LS
SR PCE Collects via BGP-LS
IGP Segments
BGP Segments
Topology
Collects information from network

## Slide 36
50
Low latency
Low bandwidth
12
11
5
IGP-1
IGP-2
10
1
13
14
4
2
3
An end-to-end path as a list of segment
SR
PCE
PCEP,Netconf, BGP
7
Peering SID: 147
Node SID: 16001
Node SID:
16002
Adj SID: 124
{16002, 124, 147}
{124, 147}
{147}
{16001, 16002, 124, 147}
BGP-Peer
Controller learn the network topology and usage dynamically
Controller calculate the optimized path for different applications: low latency, or high bandwidth
Controller just program a list of the labels on the source routers. The rest of the network is not aware: no signaling, no state information  simple and Scalable
Default ISIS cost metric: 10
High latency
High bandwidth

## Slide 38
Segment Routing
Segment Routing Global Block
MENOG 18

## Slide 39
Segment Routing Global Block
  Range of labels reserved for Segment Routing Global Segments
  Default SRGB is 16,000 – 23,999
A prefix-SID is advertised as a domain-wide unique index
The Prefix-SID index points to a unique label within the SRGB
  Index is zero based, i.e. first index = 0
  Label = Prefix-SID index + SRGB base
  E.g. Prefix 1.1.1.65/32 with prefix-SID index 65 gets label 16065
  index 65 --> SID is 16000 + 65 =16065
Multiple IGP instances can use the same SRGB or use different non-overlapping SRGBs
Segment Routing Global Block (SRGB)

## Slide 40
16000 | 
23999 | 
24000 | 
24004 | Idx 4
31999 | 
1048575 | 
16000 | 
16004 | Idx 4
23999 | 
24000 | 
1048575 | 
16000 | 
16004 | Idx 4
23999 | 
24000 | 
1048575 | 
SRGB
16000-2399
1
2
3
4
SRGB
16000-2399
SRGB
24000-31999
Recommended SRGB allocation:
Same SRGB for all
Same SRGB for all:
Simple
Predictable
easier to troubleshoot
simplifies SDN Programming

## Slide 41
Segment Routing
IGP Control and Date Plane
MENOG 18

## Slide 42
MP-BGP
PE-1
PE-2
IPv4
IPv6
IPv4
VPN
IPv6
VPN
VPWS
VPLS
LDP
RSVP
BGP
Static
IS-IS
OSPF
MPLS Forwarding
PE-1
PE-2
IGP
MPLS Control and Forwarding Operation with Segment
Routing
No changes to
control or
forwarding plane
IGP label
distribution for
IPv4 and IPv6.
Forwarding plane
remains the same
Services
Packet
Transport

## Slide 43
• IPv4 and IPv6 control plane
• Level 1, level 2 and multi-level routing
• Prefix Segment ID (Prefix-SID) for host prefixes on loopback interfaces
• Adjacency SIDs for adjacencies
• Prefix-to-SID mapping advertisements (mapping server)
• MPLS penultimate hop popping (PHP) and explicit-null label signaling
SR IS-IS Control Plane overview

## Slide 44
ISIS TLV Extensions
SR for IS-IS introduces support for the following (sub-)TLVs:
– SR Capability sub-TLV (2) IS-IS Router Capability TLV (242)
– Prefix-SID sub-TLV (3) Extended IP reachability TLV (135)
– Prefix-SID sub-TLV (3) IPv6 IP reachability TLV (236)
– Prefix-SID sub-TLV (3) Multitopology IPv6 IP reachability TLV (237)
– Prefix-SID sub-TLV (3) SID/Label Binding TLV (149)
– Adjacency-SID sub-TLV (31) Extended IS Reachability TLV (22)
– LAN-Adjacency-SID sub-TLV (32) Extended IS Reachability TLV (22)
– Adjacency-SID sub-TLV (31) Multitopology IS Reachability TLV (222)
– LAN-Adjacency-SID sub-TLV (32) Multitopology IS Reachability TLV (222)
– SID/Label Binding TLV (149)
• Implementation based on draft-ietf-isis-segment-routing-extensions

## Slide 45
SR OSPF Control Plane Overview
• OSPFv2 control plane
• Multi-area
• IPv4 Prefix Segment ID (Prefix-SID) for host prefixes on loopback interfaces
• Adjacency SIDs for adjacencies
• MPLS penultimate hop popping (PHP) and explicit-null label signaling
SR OSPF Control Plane overview

## Slide 46
OSPF adds to the Router Information Opaque LSA (type 4):
  – SR-Algorithm TLV (8)
  – SID/Label Range TLV (9)
• OSPF defines new Opaque LSAs to advertise the SIDs
  – OSPFv2 Extended Prefix Opaque LSA (type 7)
  >OSPFv2 Extended Prefix TLV (1)
  • Prefix SID Sub-TLV (2)
  – OSPFv2 Extended Link Opaque LSA (type 8)
  >OSPFv2 Extended Link TLV (1)
  • Adj-SID Sub-TLV (2)
  • LAN Adj-SID Sub-TLV (3)
• Implementation is based on
– draft-ietf-ospf-prefix-link-attr and draft-ietf-ospf-segment-routing-extensions
OSPF Extensions

## Slide 47
TLV 135
TLV 22

## Slide 48
TLV 242

## Slide 49
Sub-TLV 3
Prefix-SID
SID-Index
16
TLV 135

## Slide 50
TLV 22
Sub-TLV 32
LAN-Adj-SID
LAN-Adj-SID
24001

## Slide 51: Use Cases
MENOG 18

## Slide 52
Do More With Less
IGP
LDP
RSVP
BGP-LU
LDP
BGP
BGP-LU
LDP
BGP
BGP
IGP With SR
IGP With SR
Unified MPLS
PCE
Intra-Domain CP
FRR or TE
Intra-Domain CP
L2/L3VPN Services
EPN 5.0
Metro Fabric
Netconf
Yang
Netconf
Yang
Programmability
Provisioning

## Slide 53: IPv4/v6 VPN/Service transport
  IGP only
    No LDP, No RSVP-TE
  ECMP multi-hop shortest-path
5
7
7
5
VPN
7
5
Packet to Z
VPN
7
5
Packet to Z
VPN
7
5
Packet to Z
Packet to Z
7
VPN
Packet to Z
7
VPN
Site-1
VPN
Site-2
VPN
VPN
7
5
Packet to Z
Packet to Z
VPN
Packet to Z
PHP
PE-1
2
4
3
5
6
PE-7

## Slide 54: Internetworking With LDP
MENOG 18

## Slide 55
1
3
2
4
5
6
LDP
LDP
LDP
LDP
LDP
LDP
LDP
LDP Domain
Initial state: All nodes run LDP, not SR
Step1: All nodes are upgraded to SR
in no particular order
Default label imposition preference = LDP
Leave default LDP label imposition preference
Step2: All PEs are configured to prefer SR Label imposition
in no particular order
Step3: LDP is removed from the nodes in the network
in no particular order
Final State: All nodes run SR,Not LDP
Simplest Migration: LDP to SR
LDP+SR
LDP+SR
LDP+SR
LDP+SR
LDP+SR
LDP+SR
SR
segment-routing mpls sr-prefer
SR
SR
SR
SR
SR
SR

## Slide 56
16000 | 
16005 | pop
23999 | 
24000 | 
24003 | pop
1048575 | 
Local/in lbl
Out lbl
16000 | 
23999 | 
24000 | 
24005 | 16005
31999 | 
32011 | 24003
1048575 | 
Local/in lbl
Out lbl
16000 | 
16005 | 24005
23999 | 
24000 | 
24001 | 32011
1048575 | 
Local/in lbl
Out lbl
16000 | 
16005 | 16005
23999 | 
24000 | 
24002 | 24001
1048575 | 
Local/in lbl
Out lbl
SRGB
1
2
3
4
5
segment-routing mpls sr-prefer
segment-routing mpls (defualt)

## Slide 57
C
B
D
A
Z
LDP
SR
When a node is LDP capable but its next-hop along the SPT to the destination
is not LDP capable
  no LDP outgoing label
In this case, the LDP LSP is connected to the prefix segment
C installs the following LDP-to-SR FIB entry:
incoming label: label bound by LDP for FEC Z
outgoing label: prefix segment bound to Z
outgoing interface: D
This entry is derived and installed
automatically , no config required
Prefix | Out Label (LDP), Interface
Z | 16, 0
Input label(LDP) | Out Label (SID), Interface
32 | 16006, 1
LDP/SR Interworking - LDP to SR

## Slide 58
16000 | 
16005 | pop
23999 | 
24000 | 
Local/in lbl
Out lbl
24000 | 
16005 | 16005
31999 | 
90007 | 
Local/in lbl
Out lbl
24000 | 
90100 | 90007
Local/in lbl
Out lbl
90008 | 90100
Local/in lbl
Out lbl
SGB
1
2
3
4
5
LDP
SR
Copy
LDP LSP
????
16005
1.1.1.5/32
90007
1.1.1.5/32
lbl 90100
SID 16005
1.1.1.5/32

## Slide 59
C
B
D
A
Z
Prefix | Out Label (SID), Interface
Z | ?, 0
Input Label(SID) | Out Label (LDP), Interface
? | 16, 1
16006
LDP/SR Interworking - SR to LDP
When a node is SR capable but its next-hop along the SPT to the destination
is not SR capable
no SR outgoing label available
In this case, the prefix segment is connected to the LDP LSP
Any node on the SR/LDP border installs SR-to-LDP FIB entry(ies)
LDP
SR

## Slide 60
C
B
D
A
Z
Prefix | Out Label (SID), Interface
Z | 16006, 0
Input Label(SID) | Out Label (LDP), Interface
16006 | 16, 1
Z(16006)
LDP/SR Interworking - Mapping Server
A wants to send traffic to Z, but
  Z is not SR-capable, Z does not advertise any prefixSID
   which label does A have to use?
The Mapping Server advertises the SID mappings for the non-SR routers
  for example, it advertises that Z is 16066
A and B install a normal SR prefix segment for 16066
C realizes that its next hop along the SPT to Z is not SR capable hence C installs
an SR-to-LDP FIB entry
  incoming label: prefix-SID bound
  to Z (16066)
  outgoing label: LDP binding
  from D for FEC Z
A sends a frame to Z with a
single label: 16006
LDP
SR

## Slide 61
16000 | 
16005 | pop
23999 | 
Local/in lbl
Out lbl
16000 | 
16005 | 16005
23999 | 
Local/in lbl
Out lbl
90090 | pop
90090 | pop
Local/in lbl
Out lbl
1
2
3
4
5
LDP
SR
Mapping-Server
1.1.1.5
1.1.1.5/32
Imp-null
1.1.1.5/32
lbl 90090
16000 | 
16005 | 
23999 | 
90002 | 90090
Local/in lbl
Out lbl
NA ?
Copy
90090

## Slide 62: Traffic Protection
MENOG 18

## Slide 63
• Classic LFA has disadvantages:
– Incomplete coverage, topology dependent
– Not always providing most optimal backup path
Topology Independent LFA (TI-LFA) solves these issues
Classic Per-Prefix LFA – disadvantages

## Slide 64
Classic LFA Rules

## Slide 65
1
2
3
5
6
7
5
Default Metric : 10
Initial
Classic LFA FRR
TI-LFA FRR
Post-Convergence
Dest-1
Dest-2
Classic LFA has partial coverage
X
Classic LFA is topology dependent: not all
topologies provide LFA for all destinations
– Depends on network topology and metrics
– E.g. Node6 is not an LFA for Dest1 (Node5) on
Node2, packets would loop since Node6 uses Node2
to reach Dest1 (Node5)
Node2 does not have an LFA for this destination
(no  backup path in topology)
Topology Independent LFA (TI-LFA)
provides 100% coverage
20

## Slide 66
1
2
3
5
6
7
5
Default Metric : 10
Initial
Classic LFA FRR
TI-LFA FRR
Post-Convergence
Dest-1
Dest-2
PE-4
100
100
X
Classic LFA and suboptimal path
Classic LFA may provide a suboptimal FRR backup
path:
– This backup path may not be planned for capacity, e.g. P
node 2 would use PE4 to protect a core link, while a
common planning rule is to avoid using Edge nodes for
transit traffic
– Additional case specific LFA configuration would be needed
to avoid selecting undesired backup paths
– Operator would prefer to use the post-convergence path as
FRR backup path, aligned with the regular IGP
convergence
 TI-LFA uses the post-convergence
path as FRR backup path

## Slide 67
A
1
2
5
3
4
Z
Default metric: 10
Packet to Z
Prefix-SID Z
Packet to Z
Prefix-SID Z
Packet to Z
1000
P-Space
Q-Space
• TI-LFA for link R1R2 on R1
• Calculate LFA(s)
- Compute post-convergence SPT
- Encode post-convergence path in a SID-list
- In this example R1 forwards the packets towards R5
TI-LFA – Zero-Segment Example

## Slide 68
A
1
2
3
4
Z
Default metric: 10
Packet to Z
Prefix-SID Z
Packet to Z
Packet to Z
Prefix-SID Z
Prefix-SID (R4)
P-Space
Q-Space
TI-LFA for link R1R2 on R1
- Compute post-convergence SPT
- Encode post-convergence path in a SID-list
- In this example R1 imposes the SID-list <Prefix-SID(R4)> and sends packets towards R5
TI-LFA – Single-Segment Example
5
Packet to Z
Prefix-SID Z

## Slide 69
A
1
2
3
4
Z
Default metric: 10
Packet to Z
Prefix-SID Z
Packet to Z
1000
Packet to Z
Prefix-SID Z
Prefix-SID (R4)
Adj-SID (R4-R3)
Packet to Z
Prefix-SID Z
Adj-SID (R4-R3)
P-Space
Q-Space
Packet to Z
Prefix-SID Z
5
TI-LFA – Double-Segment Example
TI-LFA for link R1R2 on R1
- Compute post-convergence SPT
Encode post-convergence path in a SID-list
- In this example R1 imposes the SID-list <Prefix-SID(R4), Adj-SID(R4-R3)> and sends packets towards R5

## Slide 70
A
1
2
5
3
4
Z
Default metric: 10
Packet to Z
LDP (1,Z)
Packet to Z
1000
Packet to Z
Prefix-SID Z
LDP (5,4)
Adj-SID (R4-R3)
Packet to Z
Prefix-SID Z
Adj-SID (R4-R3)
P-Space
Q-Space
Packet to Z
Prefix-SID Z
TI-LFA for LDP Traffic

## Slide 71: Traffic Engineering
MENOG 18

## Slide 72
• Little deployment and many issues
• Not scalable
  – Core states in k×n2
  – No inter-domain
• Complex configuration
– Tunnel interfaces
• Complex steering
– PBR, autoroute
Does not support ECMP
RSVP-TE

## Slide 73
• Simple, Automated and Scalable
  – No core state: state in the packet header
  – No tunnel interface: “SR Policy”
  – No head-end a-priori configuration: on-demand policy instantiation
– No head-end a-priori steering: automated steering
• Multi-Domain
  – SDN Controller for compute
  – Binding-SID (BSID) for scale
• Lots of Functionality
– Designed with lead operators along their use-cases
Provides explicit routing
Supports constraint-based routing
Supports centralized admission control
No RSVP-TE to establish LSPs
Uses existing ISIS / OSPF extensions to advertise link attributes
Supports ECMP
Disjoint Path
SRTE

## Slide 74
5
14
22
9
23
3
13
7
2
21
10
11
T:30
T:30
VRF Blue
VRF Blue
Router-id of NodeX: 1.1.1.X
Prefix-SID index of NodeX: X
Link address XY: 99.X.Y.X/24 with X < Y
Adj-SID XY: 240XY
Default IGP Metric: I:10
Default TE Metric: T:10
TE Metric used to express latency
1.1.1.11
1.1.1.10
1.1.1.3
16003
1.1.1.5
16005
1.1.1.22
16022
1.1.1.7
16007
1.1.1.9
16009
1.1.1.23
16023
Domain-1
ISI-S/SR
Domain-2
ISI-S/SR
PCC
PCC
PCC
PCC
SR
PCE
Domain-1
ISI-S/SR
Domain-2
ISI-S/SR
BGP-LS
SR
PCE
PCEP
PCEP
PCEP
PCEP
BGP
BGP
BGP
BGP
RR
1.1.1.2
1.1.1.21

## Slide 75
5
14
22
9
23
3
13
7
2
21
10
11
T:30
T:30
VRF Blue
VRF Blue
SR
PCE
RR
BGP:
1.1.1.21/32
via 21
MAP: 1.1.1.21/32 in vrf BLUE must receive
low latency service  tag with
community (100:777)
VPN Label : 99999
MAP: Community (100:777) means
“minimize TE Metric” and
“compute at PCE”
PCreq/reply
BSID:
30022
COMPUTE: minimize TE Metric to Node22
RESULT: SID list: OIF: to3
Automated Steering uses color extended communities and nexthop to match with the color and end-point of an SR Policy
E.g. BGP route 2/8 with nexthop 1.1.1.1 and color 100
will be steered into an SR Policy with color 100 and end-point 1.1.1.1
If no such SR Policy exists, it can be instantiated automatically (ODN)

## Slide 76: SRv6
MENOG 18

## Slide 77: SRv6 for underlay
IPv6 for reach
RSVP for FRR/TE
Horrendous states scaling in k*N^2
SRv6 for Underlay
Simplification, FRR, TE, SDN

## Slide 78: Opportunity for further simplification
Multiplicity of protocols and states hinder network economics
IPv6 for reach
Simplification, FRR, TE, SDN
SRv6 for Underlay
Additional Protocol just for tenant ID
UDP+VxLAN Overlay
Additional Protocol and State
NSH for NFV

## Slide 79
IPV6 Header
Next Header (NH)
Indicate what comes next

## Slide 80
NH=IPv6
NH=IPv4

## Slide 81
• Generic routing extension header
  – Defined in RFC 2460
  – Next Header: UDP, TCP, IPv6…
  – Hdr Ext Len: Any IPv6 device can skip this header
  – Segments Left: Ignore extension header if equal to 0
• Routing Type field:
  > 0 Source Route (deprecated since 2007)
  > 1 Nimrod (deprecated since 2009)
  > 2 Mobility (RFC 6275)
  > 3 RPL Source Route (RFC 6554)
  > 4 Segment Routing
NH=Routing Extension

## Slide 82
NH=SRv6
  NH=43,Type=4

## Slide 83
NH=43
Routing Extension
RT = 4
Segment-List

## Slide 84
SRH Processing
MENOG 18

## Slide 85: Source Node
Source node is SR-capable
SR Header (SRH) is created with
  Segment list in reversed order of the path
    Segment List [ ] is the LAST segment
    Segment List [ ] is the FIRST segment
  Segments Left is set to
  First Segment is set to
IP DA is set to the first segment
Packet is send according to the IP DA
  Normal IPv6 forwarding
4
A4::
1
A1::
SR Hdr
IPv6 Hdr
SA = A1::, DA = A2::
( A4::, A3::, A2:: ) SL=2
Payload
2
A2::
3
A3::
Version
Traffic Class
Next = 43
Hop Limit
Payload Length
Source Address = A1::
Destination Address = A2::
Segment List [ 0 ] = A4::
Segment List [ 1 ] = A3::
Next Header
Len= 6
Type = 4
SL = 2
First = 2
Flags
TAG
IPv6 Hdr
Segment List [ 2 ] = A2::
SR Hdr
Payload
Flow Label
Flow Label
Notes: Here we assume that the source node is SR-capable.
But of course we are also able to handle cases where the source is either not SR capable or not aware that SR is used at some point in the network. In these cases the SR information can be added later on the path.
We'll see that in the use-case section
Summarized representation of the headers

## Slide 86: Non-SR Transit Node
SR Hdr
IPv6 Hdr
SA = A1::, DA = A2::
( A4::, A3::, A2:: ) SL=2
Payload
Plain IPv6 forwarding
Solely based on IPv6 DA
No SRH inspection or update
4
A4::
1
A1::
2
A2::
3
A3::
Notes: Before reaching 2, the packet may traverse a non-SR transit node.
And this is not a problem at all.
Since the IP DA is A2::, the SR H will not even be looked at before reaching 2.

## Slide 87: SR Segment Endpoints
SR Hdr
IPv6 Hdr
SA = A1::, DA = A3::
( A4::, A3::, A2:: ) SL=1
Payload
SR Endpoints: SR-capable nodes whose address is in the IP DA
SR Endpoints inspect the SRH and do:
  IF Segments Left > 0, THEN
    Decrement Segments Left ( -1 )
    Update DA with Segment List [ Segments Left ]
    Forward according to the new IP DA
Version
Traffic Class
Next = 43
Hop Limit
Payload Length
Source Address = A1::
Destination Address = A3::
Segment List [ 0 ] = A4::
Segment List [ 1 ] = A3::
Next Header
Len= 6
Type = 4
SL = 1
First = 2
Flags
TAG
IPv6 Hdr
Segment List [ 2 ] = A2::
SR Hdr
Payload
Flow Label
Flow Label
4
A4::
A
A1::
2
A2::
3
A3::
Notes: At 2 we have reached the IP Destination Address
At this point the forwarding engine will look at whatever is next in the packet

## Slide 88: SR Segment Endpoints
SR Hdr
IPv6 Hdr
SA = A1::, DA = A4::
( A4::, A3::, A2:: ) SL=0
Payload
SR Endpoints: SR-capable nodes whose address is in the IP DA
SR Endpoints inspect the SRH and do:
  IF Segments Left > 0, THEN
    Decrement Segments Left ( -1 )
    Update DA with Segment List [ Segments Left ]
    Forward according to the new IP DA
  ELSE (Segments Left = 0)
    Remove the IP and SR header
    Process the payload:
      Inner IP: Lookup DA and forward
      TCP / UDP: Send to socket
      …
Version
Traffic Class
Next = 43
Hop Limit
Payload Length
Source Address = A1::
Destination Address = A4::
Segment List [ 0 ] = A4::
Segment List [ 1 ] = A3::
Next Header
Len= 6
Type = 4
SL = 0
First = 2
Flags
TAG
IPv6 Hdr
Segment List [ 2 ] = A2::
SR Hdr
Payload
Flow Label
Flow Label
4
A4::
1
A1::
2
A2::
3
A3::
Standard IPv6 processing
The final destination does not have to be SR-capable.

## Slide 89
Deployments around the world
Bell in Canada
Orange
Microsoft
SoftBank
Alibaba
Vodafone
Comcast
China Unicom

## Slide 90: Deployments in IRAN
IRAN TIC new Network is going to be implemented based on SR

## Slide 91
Rasoul Mesghali : rasoul.mesghali@gmail.com
Vahid Tavajjohi : vahid.tavajjohi@gmail.com